## Slide 1
IE5617 Lean Concepts and Applications
Santhosh Kumar Sudhandrakumar 002541930

## Slide 2
Lean Supply Chain &
Material Flow Optimization
EV Component Manufacturing
44.8%
Lower Material
Lead Time
20.3%
Lower Average
Inventory
37.4%
Less Internal
Material Travel

## Slide 3
Business Problem
1
Inconsistent Supplier Performance
Five critical EV components sourced from five suppliers with variable lead times and quality.
2
Excess Buffer Inventory
High safety stock and long internal waiting time increase working capital.
3
Avoidable Material Travel
Receiving, inspection, storage, and line replenishment include inconsistent work methods.
4
Goal
Build a Lean supplier-to-production flow that improves supply assurance, quality, and responsiveness.

## Slide 4
Project Approach
Value → Value Stream → Flow → Pull → Perfection
MEASURE
12 months of simulated operating data across 60 supplier-month observations.
DIAGNOSE
Supplier scorecards, lead-time variability, defect rate, and Value Stream Mapping (VSM).
DESIGN
Kanban pull replenishment, 6S, point-of-use flow, standardized work, and quality controls.
CONTROL
Recurring KPI reviews, visual management, audits, and continuous-improvement actions.

## Slide 5
Supplier Performance Snapshot
Chart: On-Time Delivery Rate (%)
| VoltCell | DriveCore | PowerLogic | ThermaFlow | AutoSense
On-Time Delivery % | 42 | 33 | 33 | 25 | 17
Chart: Defect Rate (%)
| VoltCell | DriveCore | PowerLogic | ThermaFlow | AutoSense
Defect Rate % | 2.03 | 5.03 | 3.32 | 6.03 | 1.23
Key finding: ThermaFlow Industries has the highest defect rate (6.03%); VoltCell Components has the strongest composite supplier score (69.8 / 100).

## Slide 6
Current-State Value Stream
Chart: Process vs. Waiting Time by Step (minutes)
| Inbound Unloading | Receiving & Documentation | Quality Inspection | Storage / Put-away | Line Replenishment | Production Delivery
Process Time (min) | 35 | 25 | 40 | 30 | 28 | 20
Waiting Time (min) | 55 | 40 | 95 | 65 | 70 | 35
538 min
Total lead time
360 min
Total waiting
775 m
Material travel
Largest queue occurs at Quality Inspection (95 min wait).

## Slide 7
Lean Future-State Design
6S
Labeled storage zones, standard locations, visual controls, and routine audits.
FLOW
Reduce queues; reposition high-frequency components closer to point of use.
PULL
Kanban cards trigger replenishment from actual consumption, not forecasts.
QUALITY
Supplier defect tracking, SPC thinking, and corrective-action reviews.
STANDARD WORK
Common receiving, inspection, put-away, and replenishment procedures.
PERFECTION
Recurring scorecard and KPI reviews feed continuous-improvement events.

## Slide 8
Kanban & Inventory Planning
Chart: Current vs. Proposed Inventory by Component (units)
| Battery Module | Motor Assembly | Inverter | Cooling Module | Sensor Kit
Current Inventory | 1056 | 1280 | 887 | 1123 | 674
Proposed Inventory | 800 | 1000 | 700 | 900 | 600
20.3%
reduction in average
inventory
(5,019 → 4,000 units)
Sizing uses average daily demand, supplier lead time, and a 15% safety factor with fixed container quantities.

## Slide 9
Current vs. Future State
Chart: Current vs. Future State KPIs
| Lead Time (min) | Waiting Time (min) | Travel (m)
Current | 538 | 360 | 775
Future | 297 | 155 | 485
Lead Time
44.8%
Waiting Time
56.9%
Travel Distance
37.4%
Value-Added Ratio
22.9% → 34.3%

## Slide 10
Implementation Roadmap
1
Phase 1
Baseline & Align
Validate process times, supplier metrics, and cross-functional ownership.
2
Phase 2
Pilot
Launch 6S + Kanban for one high-volume component; monitor shortages and inventory.
3
Phase 3
Scale
Extend standardized work and pull replenishment to remaining components.
4
Phase 4
Control
Supplier scorecards, KPI boards, audits, and continuous-improvement backlog.

## Slide 11
Project Impact & Takeaway
Analyzed 5 suppliers, 5 critical components, and 6 internal material-flow steps
Modeled a 44.8% reduction in supplier-to-production material lead time
Modeled a 20.3% reduction in average inventory using Kanban pull replenishment
Reduced modeled internal material travel by 37.4% through future-state redesign
Applied Lean, VSM, Kanban, 6S, supplier scorecards, and continuous improvement